## Slide 1: Lessons In Electric and Electronic Circuits dr Abdulazeez Ali Mechatronic Dept. ISHIK UNIVERSITY

## Slide 2: Contents
A. Electric ccts B. Electronics
1 BASIC CONCEPTS OF ELECTRICITY 1. Introduction
2 OHM’s LAW 2.Semiconductor physics.
3. Basic Electrical Elements? 3.BJT Transistor.
4. Kirchoff”s Law 4. Photo Transistor and optpisolators
5. Mesh current 5. FET Transistors
6. Node voltage
7. Introduction to network
8. Millman’s Theorem References
9. Superposition Theorem 1.. Electric Circuits, By Tony R. Kuphaldt .
10. Thevenin’s Theorem 2. Electronic principles, Elbert Malvino
11. Norton’s Theorem and David Bates.
12 Alternating current Circuits.
13. Maximum Power Transfer Theorem
14. ∆-Y and Y-∆ conversions .

## Slide 3: CHAPTER ONE INTRODUCTION
1.1 . BASIC CONCEPTS OF ELECTRICITY
It was discovered centuries ago that certain types of materials would mysteriously attract one another after being rubbed together.
For example: after rubbing a piece of silk against
a piece of glass, the silk and glass would tend to
stick together. Indeed, there was an attractive
force that could be demonstrated even when the two materials were
separated:
Paraffin wax and wool cloth are another
pair of materials early experimenters
recognized as manifesting attractive
forces after being rubbed together:

## Slide 4
This phenomenon became even more interesting when it was discovered that identical materials, after having been rubbed with their respective cloths, always repelled each other:
It was also noted that when a piece of glass rubbed with silk was exposed to a piece of wax rubbed with wool, the two materials would attract one another:

## Slide 5
One pioneering researcher, Benjamin Franklin, came to the conclusion that there was only one fluid exchanged between rubbed objects, and that the two different ”charges” were nothing more than either an excess or a deficiency of that one fluid.
After experimenting with wax and wool, Franklin suggested that the coarse wool removed some of this invisible fluid from the smooth wax, causing an excess of fluid on the wool and a deficiency of fluid on the wax.
The resulting disparity in fluid content between the wool and wax would then cause an attractive force, as the fluid tried to regain its former balance between the two materials.
The type of charge that was associated with rubbed wax became known as ”negative” (because it was supposed to have a deficiency of fluid).
while the type of charge associated with the rubbing wool became known as ”positive” (because it was supposed to have an excess of fluid).
Little did he know that his innocent conjecture would cause much confusion for students of electricity in the future!
HA HA HA HA….

## Slide 6
Precise measurements of electrical charge were carried out by the French physicist Charles Coulomb in the 1780’s using a device called a torsional balance measuring the force generated between two electrically charged objects.
The results of Coulomb’s work led to the development of a unit of electrical charge named in his honor, the coulomb.
If two ”point” objects (hypothetical objects having no appreciable surface area) were equally charged to a measure of 1 coulomb, and placed 1 meter (approximately 1 yard) apart, they would generate a force of about 9 billion newtons (approximately 2 billion pounds), either attracting or repelling depending on the types of charges involved.

## Slide 7
It was discovered much later that this ”fluid” was actually composed of extremely small bits of matter called electrons., another material exhibiting charged properties when rubbed with cloth.
Experimentation has revealed that all objects are composed of extremely small ”building-blocks” known as atoms, these atoms are in turn composed of smaller components known as particles.
Three fundamental particles comprising most atoms are called protons, neutrons and electrons.
Atoms are far too small to be seen,
but if we could look at one, it
might appear something like this:

## Slide 8
There’s actually a lot of empty space between the electrons and the cluster of protons and neutrons residing in the middle.
In any atom, the protons and neutrons are very tightly bound together, which is an
important quality.
The tightly-bound clump of protons and neutrons in the center of the atom
is called the nucleus.
the number of protons in an atom’s nucleus determines its elemental
identity.
However, electrons have significantly more freedom to move around in an atom than either
protons or neutrons.
Electrons and protons are unique in the fact that they are attracted to one another over a
distance. It is this attraction over distance which causes the attraction between rubbed
objects, where electrons are moved away from their original atoms to reside around atoms
of another object.
That is, each electron has a negative charge, and each proton a positive charge. In equal numbers within an atom, they counteract each other’s presence so that the net charge within the atom is zero.

## Slide 9
That is, each electron has a negative charge, and each proton a positive charge. In equal numbers within an atom, they counteract each other’s presence so that the net charge within the atom is zero.
The result of an imbalance of this ”fluid” (electrons) between objects is called static electricity.
It is called ”static” because the displaced electrons tend to remain stationary after being moved from one insulating material to another.

## Slide 10
REVIEW:
All materials are made up of tiny ”building blocks” known as atoms.
All naturally occurring atoms contain particles called electrons, protons, and neutrons,
Electrons have a negative (-) electric charge.
Protons have a positive (+) electric charge.
Neutrons have no electric charge.
Electrons can be dislodged from atoms much easier than protons or neutrons.
The number of protons in an atom’s nucleus determines its identity as a unique element.

## Slide 11: 2. Conductors, insulators, and electron flow
The electrons of different types of atoms have different degrees of freedom to move around.
With some types of materials, such as metals, the outermost electrons in the atoms are so loosely bound that they chaotically move in the space between the atoms of that material bynothing more than the influence of room-temperature heat energy. Because these virtually unbound electrons are free to leave their respective atoms and float around in the space between adjacent atoms, they are often called free electrons.
In other types of materials such as glass, the atoms’ electrons have very little freedom to move around. While external forces such as physical rubbing can force some of these electrons to leave their respective atoms and transfer to the atoms of another material, they do not move between atoms within that material very easily.

## Slide 12
This relative mobility of electrons within a material is known as electric conductivity.
. Materials with high electron mobility (many free electrons) are called conductors, :
silver, copper, gold, aluminum, iron, steel, brass,….
materials with low electron mobility (few or no free electrons) are called insulators.
Glass, rubber, oil, asphalt, fiberglass,
porcelain, ceramic, quartz ……..

## Slide 13: 3. Basic Electrical Elements
When electrons move, they produce an electrical current,
The reason they move is that we impose an electrical field that imparts energy by doing work on the electrons.
A measure of the electric field’s potential is called voltage.
The resulting movement of electrons is the current
Current is defined as the time rate of flow of charge:
I(t) = dq / dt
where I denotes current and q denotes quantity of charge
The SI unit for current is the ampere (A), and charge is measured in coulombs (C = A · s).
Voltage is sometimes referred to as electromotive force, or emf.

## Slide 14
An electrical circuit is a closed loop consisting of several conductors connecting electrical components.

## Slide 15
The terminology and current flow convention used in the analysis of an electrical circuit are illustrated in Figure

## Slide 16
There are three basic passive electrical elements: the resistor ( R ) , capacitor ( C ), and inductor ( L ).
Passive elements require no additional power supply, unlike active devices such as integrated circuits
Resistor
is a dissipative element that converts electrical energy into heat.
Ohm’s law defines the voltage-current characteristic of an ideal resistor:
V = I R

## Slide 17
If a resistor’s material is homogeneous and has a constant cross-sectional area, then the resistance is given by
R = ρL / A …2,3
where is the resistivity, or specific resistance
of the material; L is the wire length;
and A is the cross-sectional area.
Example:

## Slide 18
Capacitor
A capacitor is a passive element that stores energy in the form of an electric field. This field is the result of a separation of electric charge.
direct current (DC) does not flow through a capacitor; rather, charges are displaced
from one side of the capacitor through the conducting circuit to the other side,
establishing the electric field. The displacement of charge is called a displacement
current because current appears to flow through the device as it charges or discharges.

## Slide 19
The capacitor’s voltage-current relationship is defined as:
where q ( t ) is the amount of accumulated charge measured in coulombs and C is the capacitance measured in farads (F coulombs/volts).
By differentiating this equation, we can relate the displacement current to the rate of change of voltage:
Inductor
An inductor is a passive energy storage element that stores energy in the form of a magnetic field. The simplest form of an inductor is a wire coil, which has a tendency to maintain a magnetic field once established. The inductor’s characteristics are a direct result of Faraday’s law of induction, which states V(t) = dλ /dt
where λ is the total magnetic flux through the coil windings due to the current. Magnetic flux is measured in Webers (Wb).

## Slide 20
The magnetic field lines
surrounding an inductor
For an ideal coil, the flux is proportional to the current:
λ = LI
where L is the inductance of the
coil, which is assumed to be
Constant.
The unit of measure of inductance is the henry (H = Wb/A).
inductor’s voltage-current relationship can be expressed as
V(t) = L dI / dt
voltage across an inductor is proportional to the rate of change of the current through the inductor.
Integrating Equation
current
through an inductor cannot change instantaneously

## Slide 21: 4. Kirchhoff’s Laws
4.1 Kirchhoff’s voltage law (KVL) states that the
sum of voltages around a closed loop or path is 0
To apply KVL to a circuit,
first assume a current direction on
each branch of the circuit.
assign the appropriate polarity to
the voltage across each passive element

## Slide 22
KVL will be used to find the current IR in the following circuit.
The first step is to assume the current direction for IR .
Starting at point A and progressing clockwise around the loop, we
assign the first voltage sign we come to on each element yielding
− Vs + VR = 0
Applying Ohm’s law, − Vs + IRR = 0
Therefore,
IR = Vs ⁄ R = 10 ⁄ 1000 A = 10 mA

## Slide 23
4.1 Kirchhoff’s current law (KCL) states that the sum of the currents flowing into a closed surface or node is 0.
I1 + I2 − I3 = 0
More generally,

## Slide 24: 4.2 Series Resistance Circuit
Applying KVL to the simple series resistor circuit illustrated in Figure yields some useful results. Assuming a current direction I, starting at node A, and following a clockwise direction yields
– Vs + VR1 + VR2 = 0
From Ohm’s law,
VR1 = IR1 and VR2 = IR2
Substituting these two equations into above
Equation gives
− Vs + IR1 + IR2 = 0 and solving for I yields:
if we had a single resistor of value R1 + R2 ,
we would have the same result.
Therefore resistors in series add, and the equivalent resistance of a series
resistance circuit is Req = R1 + R2 or

## Slide 25
By applying KVL to capacitor and inductor circuits it can be shown that: two capacitors in series combine as:
and two inductors in series add:
A circuit containing two resistors in series is referred to as a voltage divider because the source voltage Vs divides between each resistor.
Expressions for the resistor voltages
can be obtained:
In general, for N resistors connected in series with a total applied voltage
Of Vs , the voltage Vri across any resistor Ri is:
Voltage dividers are useful because they allow us to create different reference voltages in a circuit even if the circuit is energized only by a single output supply.

## Slide 26: 4.3 Parallel Resistance Circuit
Applying KCL to the simple parallel resistor circuit illustrated in Figure , also yields some useful results. Because each resistor experiences the same voltage Vs , as they are both in parallel with the source, Ohm’s law gives
I1 = Vs / R1 and I2 = Vs / R2
Applying KCL at node A gives
I – I1 – I2 = 0
Substituting the currents from Equations yields
Replacing the resistance values R1 and R2 with their conductance equivalents 1/ G1 and 1/ G2 gives

## Slide 27
In general, N resistors connected in parallel can be replaced by a single equivalent resistance given by
By applying KCL to capacitor and inductor circuits, it can be shown that two capacitors in parallel add:
Ceq = C1 + C2
and two inductors in parallel combine as
A circuit containing two resistors
connected in parallel is called a current
divider

## Slide 28
Example: consider the following network, where the goal is to find Iout and Vout.
Solution using the series R2 and R4 resistances.
this is in parallel with resistor R3 .
Resistors R5 and R6 are also in parallel.
Formulas:
Applying KVL to the left loop gives
V1 = IoutR1 so Iout = V1/R1 = 10 V /1 kΩ = 10 mA
Applying KVL to the right loop
Vout = V1 – V234 = 14.2 V

## Slide 29: 5. THEVENIN AND NORTON EQUIVALENT CIRCUITS Sometimes, to simplify the analysis of more complex circuits, we wish to replace voltage sources and resistor networks with an equivalent voltage source and series resistor
Thevenin’s theorem: states that, given a pair of terminals in a linear network, the network may be replaced by an ideal voltage source VOC in series with a resistance RTH
VOC is equal to circuit voltage across the terminals
RTH is the equivalent resistance across the terminals when independent voltage sources are shorted and independent current sources are replaced with open circuits.
VOC is found by disconnecting
the rest of the circuit and
determining the voltage across
the terminals of the remaining
open circuit

## Slide 30
the voltage divider rule gives
Example illustrating Thevenin’s theorem
Thevenin equivalent circuit.
Norton equivalent
the current that would flow through the terminals if they were shorted together
ISC is found by calculating
The Thevenin and Norton equivalents are independent of the remaining circuit
network representing a load.

## Slide 31
Unfortunately, real sources and meters have terminal characteristics that are somewhat different from the ideal cases. However, the terminal characteristics of the real sources and meters can be modeled using ideal sources and meters with their associated input and output resistances.
6. VOLTAGE AND CURRENT SOURCES
AND METERS
■ An ideal voltage source has zero output resistance and can supply infinite current.
■ An ideal current source has infinite output resistance and can supply infinite voltage.
■ An ideal voltmeter has infinite input resistance and draws no current.
■ An ideal ammeter has zero input resistance and no voltage drop across it.

## Slide 32
.
Real voltage source with output
impedance
Real current source with output impedance
When a load is attached to the source and current flows, the output voltage Vout will
be different from the ideal source voltage V s due to voltage division.
When a load is attached to the source, the source current Is divides between the output impedance and the load.

## Slide 33
The simple attenuator circuit is attached to a voltmeter input. The
input-output relation for the above circuit without a load is
The KVL equation written around the leftmost loop has vin= v1 + vout ; substituting for
v1, we find

## Slide 34
We can not measure voltages reliably unless the measurement device has little effect on what we are trying to measure. what we need is :
Example a- find Rtotal b. Find Thevenen Equivelant c. Find Norton Eq.

## Slide 36
RL must equal (25 ) for maximum power transfer.

## Slide 37: 7. ALTERNATING CURRENT CIRCUIT ANALYSIS
A sinusoidal AC voltage V ( t ) is illustrated in
Figure 2.28 and can be expressed mathematically as
V(t) = Vm sin(ωt + φ)
where Vm is the signal amplitude,
ω is the radian frequency measured in radians per second
φ is the phase angle measured in radians.
The phase angle is related to the time shift (Δ t ) between the signal and reference:
φ = ωΔt

## Slide 38
A positive phase angle implies a leading waveform, and a negative angle implies a lagging waveform .
The period T of the waveform is the time required for a full cycle.
The frequency of the signal, measured in hertz (Hz cycles/sec), is related to the period and radian frequency as
DC offset. It represents the vertical shift of the signal from the reference
sinusoid. Mathematically, the DC offset is represented by the term Vdc in the equation:

## Slide 39
EXAMPLE : For the following AC signal find; Amplitude, Frequency (in radians and Hz), and the phase angle.
V(t) = 5.00 sin (t − 1) V
Solution:
The signal amplitude is Vm = 5.00 V
The signal radian frequency is ω = 1.00 rad/sec
ω is the coefficient of the time variable t in the argument of the sinusoid. Likewise, the frequency in hertz is
and the phase angle is Ø = −1 rad = −57.3°
The negative phase indicates the signal lags (i.e., occurs later in time relative to) the reference (sin(t)). The arguments of the sinusoids are always assumed to be specified in radians for computational purposes.

## Slide 40: Why Alternating current power is used in many applications where direct current(DC) power is impractical or infeasible?
a. AC power is more efficient to transmit over long distances because it is easily transformed to a high-voltage, low-current form, minimizing power losses during transmission.
b. In residential areas, it is easily transformed back to required levels.
c. Note that the voltage drop in the transmission line is small compared to the voltage level at the source.
d. AC power is easy to generate with rotating machinery (generator).
e. AC power is easy to use to drive rotating machinery (e.g. motor).
f. AC power provides a fixed frequency signal (60 Hz in the United States, 50 Hz in Europe) that can be used for timing purposes and synchronization.

## Slide 41
The steady state analysis of AC circuits is simplified by the use of phasor analysis, which uses complex numbers to represent sinusoidal signals.
Euler’s formula forms the basis for this analysis:
Circuit variables V and I treated as complex exponentials with magnitudes Vm and Im and phase for a “steady state” analysis.
A phasor (e.g., voltage V ) is a vector representation of the complex exponential:
is the complex exponential form,
is the polar form,
Vm [cos(ω t ) + j sin (ω t )] is the complex rectangular form

## Slide 42
Useful mathematical relations for manipulating complex numbers and phasors include

## Slide 43
Ohm’s law V = ZI Z : is called the impedance
voltage will lead current
g by 90 degrees
voltage will lag the current
by 90 degrees
For the capacitor, because I = C dV / dt

## Slide 44
EXAMPLE: Find the steady state current I through the capacitor in the following circuit:
Solution:
V in = 5 cos (3000t + π/2) V,
ω = 3000 rad/sec
phasor and complex form of the source is
Vin = 5 〈90°〉 V = (0 + 5j ) V
ZC = –j ⁄ ωC = –1666.67j Ω = 1666.67 〈–90°〉 Ω
ZL = jωL = 1500j Ω = 1500 〈90°〉 Ω
R2 + ZL = (3000 + 1500j)  = 3354.1 〈26.57° 〈 
Impedance of parallel combination:
_(_ R_2_ +_ _ Z_L )_ Z_C_ = Zp
( R2 + ZL ) + ZC
The numerator is:
(R2 + ZL)ZC = 3354.1 〈26.57° 〈 * 1666.67 〈–90°〉 Ω = 5,590,180 〈 63.43° 〈 
The denominator (R2 + ZL) + ZC = ((3000 + 1500j) − 1666.67j) = (3000 - 166.67j) 
= (3004.63 〈3.18°〉 Ω
Therefore Zp is equal to:

## Slide 45
The rectangular form is equal to
so the capacitor current leads the input reference by 159.8 or 2.789 rad, and the resulting current is: I(t) = 2.22 cos (3000t + 2.789) mA

## Slide 46: 8. POWER IN ELECTRICAL CIRCUITS
All circuit elements dissipate, store, or deliver power through the physical interaction between charges and electromagnetic fields.
The infinitesimal work (d W ) done when an infinitesimal
charge (d q ) moves through an electric field resulting in a change in potential represented by a voltage V. This infinitesimal work is given by
dW = V dq
Because power is the rate of work done,
P = dW/dt = V dq / dt = VI
power consumed or generated by an element
is simply the product of the voltage
across and the current through the
element.power in a resistive circuit
P = VI R = ⁄R

## Slide 47
For AC signals, because V = Vm sin(ω t + ØV ) and I = Im sin( ωt - ØI ),
Instantaneous Power is not a useful quantity by itself, but if we look at the average power delivered over a period, we get a good measure of the circuit’s or component’s overall power characteristics
The average power over a period is
where θ is the difference between the voltage and current phase angles
( ØV - ØI ), which is the phase angle of the complex impedance Z = V / I.
If we use the rms, or root-mean-square values of the voltage and current defined by

## Slide 48
the average AC power consumed by a resistor can be expressed in the same form as with DC circuits

## Slide 49: 9.TRANSFORMER
A transformer is a device used to change the relative amplitudes of voltage and current in an AC circuit.
The primary and secondary
voltages ( VP and VS ) are related by
If NS > NP , the transformer
is called a step-up transformer
If NS < NP , it is called a step-down transformer.
If NS NP , it is called an isolation transformer
IPVP = ISVS

## Slide 50: 10. IMPEDANCE MATCHING
we must be careful when connecting different devices and circuits together.
Signal termination
Impedance matching is important in applications where it is desired to transmit maximum power to a load from a source.

## Slide 51
Consider the circuit
Therefore, the power transmitted to the load is
To find the load resistance that maximizes this power, we set the derivative of the power equal to 0 and solve for the load resistance:
Hence RL = Rs